## Slide 1: The Development of different wheel robot system
Presented By LEE Lok Yin, Edmund
17 November 2020

## Slide 2: Content
ELEC3300 Project - 2D Hologram Fan
HKUST Robotics Team - Robocon
CSE Final Year Project - Indoor Guiding System for the Visually Impaired

## Slide 3
ELEC3300
2D Hologram Fan

## Slide 4: Why?
Data Transmition Speed (Main reason)
  20 x 160 pixels 0.96 inch TFT
  12Bit RGB
  At least 4 TFT is needed
  12Hz Display
  Sperate to 360 sectors
  20*160*12*4*12*360 = 663Mbit/s !!! Even I am using direct memory access(DMA)
Brightness Problem
  TFT 500 Nits
  LED 4500 Nits

## Slide 6: The 2D Hologram Fan
Fan Speed Control
Alarm
Real Time Clock
Logo Display
TFT & Buttons Control

## Slide 7: Mechanical Parts
DC Motor
Rotary Encoder
Wire Connection Rotary Joint

## Slide 8: Electronics
STM32F405RGT6
WS2812b LED
Customized PCB
DC Motor Driver
SD Card Reader

## Slide 9: Control UI
2.9 inch TFT
Buzzer
Bluetooth
Buttons
Joystick

## Slide 10: Programming
PID for Fan Speed
  PWM as output
  Encoder as input
Protocol
  SPI for TFT & SD card
  GPIO for LEDs & Buttons & Motor & Encoder
  UART for Bluetooth
  ADC for Joystick

## Slide 11: Programming
Display
  Image decoding
  GPIO Sequence Genaration
  Fast switching
1 1 1 1 0000 0000
0000 0000 0000
R G B
1 1 1 1 1 1 1 1 1 1 1 1
1 1 1 1 0000 0000
0000 0000 0000
1 1 1 1 1 1 1 1 1 1 1 1